## Slide 1
Anatomy-adaptive, expert-reviewed ONFH ROI workflow (V3.1 research)
1
CT + head mask
DICOM → real HU
TotalSegmentator
Affected-side head extraction
2
Sphere geometry + priors
Fit center and radius
Subchondral distance / radial depth
Anterosuperior weight-bearing zone
3
Patient-adaptive evidence
Cancellous reference: -100 to 600 HU
P20 low-density core
P85 sclerotic rim
6
Research features + export
θ
3D Kerboul-like angle
Subchondral / weight-bearing involvement
Experimental feature score
STL + JSON/CSV → FEA
5
Morphology + QC
✓
Connectivity, small components and hole filling
Leakage, fragments and empty-ROI checks
Expert review and correction
4
Seeded region growing
Foreground: low-density core
Background: cortex + normal cancellous bone
HU, location, rim and gradient costs
Clinical validation: Dice · Jaccard · HD95 · average surface distance · volume difference · ICC · Bland-Altman · runtime/correction time
Research use only; the experimental feature score is not a collapse probability, ARCO stage, or treatment threshold.